## Slide 1: UNIT 1
Lab Skills & Review

## Slide 2: Physics is…………
Empirical

## Slide 3
Physics must be validated through experiments.
All experiments follow this format…………

## Slide 4: The Scientific Method
Problem or Observation/Questions
2. Hypothesis
3. Experiment
4. Analysis/Conclusion

## Slide 5: 2 Terms of Interest under Analysis
Accuracy – Comparison of your results to
  A standard value
  % error =
  Another experimental value
  % error =
Precision or Uncertainty – degree of consistency of measurements or the confidence in your measurements
lamda
δ

## Slide 6: Accuracy – What prevents us from getting the “correct” value in an experiment?
Error
3 types
Personal
Caused by carelessness
Never discussed in conclusion
Systematic
Reproducible inaccuracy
Caused by an instrument or other factor that can be corrected
Random
Unpredictable, unknown variations
Cannot be eliminated
Experiment should be redone
All error is in the same direction
The experiment should be redone
Use statistical analysis to communicate this type of error

## Slide 7: How is Random Error communicated for various situations?
Single Measurement Uncertainty
Uncertainty = ½ (least count of the instrument)
Example
Bob steps on a scale with divisions of 1 lb. and the scale reads 142 lbs. What is the proper way of communicating Bob’s weight (including uncertainty)?
Answer
Bob’s weight must be higher than 141.5 or the scale would read 141 lbs. Bob must also be less than 142.5 or the scale would read 143 lbs. So Bob’s weight is 142.0 ± 0.5 lbs.

## Slide 8: Single measurements continued…
Fractional
Fractional Uncertainty =
Bob’s fractional uncertainty =
0.5/142.0 = 0.0035

## Slide 9: Single measurements continued…
Percentage
Percent Uncertainty = x 100
Bob’s Percent Uncertainty =
0.35%

## Slide 10: Single measurements continued…
Fluctuating Machine
Uncertainty = ½ Range of Fluctuation
Example
An electronic balance is fluctuating between readings of 153.25 g and 154.12 g. What is the correct way to record this measurement?
Answer
Find the average: Ave = (153.25 + 154.12)/2 = 153.69
Find the uncertainty: Uncertainty = ½(154.12 – 153.25) = 0.44
The correct measurement: (153.69 ± 0.44) g

## Slide 11: Small number of trials
Find the Mean (Average) value
Find the Uncertainty
Uncertainty = |Largest Deviation from the Mean|
Example
Joe is making banana cream pies. The recipe calls for 16.0 oz of mashed banana. Joe’s measurements are 15.5 oz, 16.4 oz, 16.1 oz, 15.9 oz, and 16.6 oz. What is Joe’s average measurement of mashed banana? What is the uncertainty in his measurements?
Answer
Find the average value: Ave = 16.1 oz
Find the largest deviation: Uncertainty = 0.6 oz
Joe’s measurement = (16.1 ± 0.6) oz of mashed banana

## Slide 12: Large number of Trials
Find the Mean Value
Find the Uncertainty
Uncertainty = Standard Deviation
σ =
This method gives greater weight to values further from the mean.

## Slide 13: Large number of trials
Back to Joe……
We know his mean value: 16.1 oz
Let’s find the standard deviation…
σ =
= 0.7 oz
Statistics show that 68.3% of your data should be in the range of ±σ and 95.5% of your data should be in the range of ±2σ.

## Slide 14: Standard Error
When comparing groups of data…
Standard Error
ά =

## Slide 15: Combining Uncertainties
For Calculated Values
Adding/Subtracting
Simply add the uncertainties
Example
Ralph’s height was measured with a tape measure to be (186 ± 2)cm. Ralph has a bug on the top of his head. The bug’s height (measured with a vernier caliper) is (0.020 ± 0.003)cm. What is the total height of Ralph and the bug?
Answer: (186.020 ± 2.003)cm

## Slide 16: Combining Uncertainties
Multiplying/Dividing
Add the fractional or percentage uncertainties
Example: The length of a rectangle is measured to be (53.3 ± 0.5) cm and the width is measured to be (8.7 ± 0.5) cm. What is the area of the rectangle?
Answer:
Mean area value: 463.7 cm2
Find the fractional uncertainties:
Length = 0.5/53.3 = 0.009
Width = 0.5/8.7 = 0.0575
Total = 0.066
Uncertainty = (463.7)(0.066) = 30.6 cm2
Area = (463.7 ± 30.6) cm2

## Slide 17
 | Al | Beth | Carl | Dee
Trial 1 | 7.83 ± 1.60 | 9.53 ± 0.27 | 8.70 ± 0.04 | 9.72 ± 0.04
Trial 2 | 11.61 ± 2.18 | 9.38 ± 0.12 | 8.75 ± 0.01 | 9.86 ± 0.10
Trial 3 | 8.85 ± 0.58 | 8.87 ± 0.39 | 8.77 ± 0.03 | 9.70 ± 0.06
Accuracy, Uncertainty, Error
Each of the following persons experimentally determined the value for the acceleration due to gravity in three trials. The accepted value for gravity is 9.80 m/s2. What can you tell me about each person’s results (accuracy, uncertainty, error)?